## Slide 1
Constructive Computer Architecture
Interrupts/Exceptions
Arvind
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology

## Slide 2: Hardware Software Interactions
Modern processors cannot function without some resident programs (“services”), which are shared by all users
Usually such programs need some special registers which are not visible to the users
Therefore all ISAs have extensions to deal with these special registers
Furthermore, these special registers cannot be manipulated by user programs; therefore user/privileged mode is needed to use these instructions
application
application
Operating system
Hardware
Application binary interface (ABI)
Supervisor binary interface (SBI)

## Slide 3: Interrupt (aka Trap) altering the normal flow of control
An external or internal event that needs to be processed by another (system) program. The event is usually unexpected or rare from program’s point of view.
program
HI1
HI2
HIn
interrupt
handler
Ii-1
Ii
Ii+1
Notes: For precise interrupt/exception, the branching out and back should be shown as ‘in-between instructions’.
Even if I_i is a page fault, the exception is between I_i-1 and I_i, not on I_i.

## Slide 4: Interrupts caused by an external event
External asynchronous event
  input/output device service-request/response
  timer expiration
  power disruptions, hardware failure
After the processor decides to process the interrupt
  It stops the current program at instruction Ii, completing all the instructions up to Ii-1 (Precise interrupt)
  It saves the PC of instruction Ii in a special register
  It disables interrupts and transfers control to a designated interrupt handler running in the privilege mode
    Privileged/user mode to prevent user programs from causing harm to other users or OS

## Slide 5: Exceptions caused by the execution of an instruction
The instruction cannot be completed
  undefined opcode, privileged instructions
  arithmetic overflow, FPU exception
  misaligned memory access
  virtual memory exceptions: page faults, TLB misses, protection violations
System call: Deliberately used by the programmer to invoke a kernel service
  Either the faulting condition is fixed; or the instruction is emulated by the exception handler; or the program is aborted
  The pipeline must undo any partial execution and record the cause of the exception
Notes: Exception instruction might need to restart (page fault) or be skipped (emulated mult). The handler adjusts the EPC depending on the situation.
I implemented Syscall as an exception itself (so not completed) and is skipped by the handler.

## Slide 6: Interrupt* handling
When an interrupt is caused
  Hardware saves the information about the interrupt in CSRs:
    mepc – exception PC
    mcause – cause of the exception
    mstatus.mpp – privilege mode of exception
    ...
  Processor jumps to the address of the interrupt handler (stored in the mtvec CSR) and increases the privilege level
A interrupt handler, a software program, takes over and performs the necessary action
*From now on, interrupts and exceptions are used interchangeably

## Slide 7: Software for interrupt handling
Hardware transfers control to the common software interrupt handler (CH) which:
  Saves all GPRs into known memory locations
  Passes mcause, mepc, stack pointer to the IH (a C function) to handle the specific interrupt
  On the return from the IH, writes the return value to mepc
  Loads all GPRs from the memory
  Execute mret, which does:
    set pc to mepc
    pop mstatus (mode, enable) stack
IH
IH
IH
CH
1
2
3
4
5
GPR
a new instruction

## Slide 8: Saving GPRs
Operating system manages the space where GPRs are saved and provides a pointer to the space for the current program
  For simplicity we’ll assume this location is fixed at GPR_BASE
RISC-V’s memory instructions require the base address to be stored in a GPR
  Therefore before GPRs can be saved, we need to free up a GPR (say x1) by storing its value in a special scratch register (mscratch)
  After saving the other GPRs, they are freed up
Finally, x1 needs to be restored from mscratch and saved
another CSR

## Slide 9: Common Interrupt Handler- SW (RISC-V Assembly)
common_handler: # entry point for exception handler # save x1 to mscratch to free up a register
csrw mscratch, x1 # write x1 to mscratch
# get the pointer for storing GPRs
li x1, GPR_BASE
# save x2 - x31
sw x2, 8(x1)
sw x3, 12(x1)
...
sw x31, 124(x1)
# now registers x2 – x31 are free
# save original x1 (now in mscratch)
csrr x2, mscratch # x2 used as temporary register
sw x2, 4(x1) # x1 still points to GPR storage

## Slide 10: Common handler- SW cont. Setting up and calling IH_Dispacher
common_handler:
... # we have saved all GPRs to stack
# call C function to handle interrupt
csrr a0, mcause # arg 0: cause
csrr a1, mepc # arg 1: epc
li a2, GPR_BASE # arg 2: pointer to all saved GPRs
... # set up stack pointer for C-code
jal ih_dispatcher # calls ih_dispatcher which may
# have been written in C
# return value is the PC to resume
csrw mepc, a0
# restore mscratch and all GPRs
li x1, GPR_BASE;
lw x2, 8(x1); lw x3, 12(x1); ...; lw x31, 124(x1)
lw x1, 4(x1) # restore x1 last
mret # finish handling interrupt

## Slide 11: IH Dispatcher (in C) Dispatches to a specific handler based on “cause”
long ih_dispatcher(long cause, long epc, long *regs) {
// regs[i] refers to GPR xi stored in stack
if(cause == 0x02) // illegal instruction
return illegal_ih(cause, epc, regs);
else if(cause == 0x08) // system call
return syscall_ih(cause, epc, regs);
else ... // other causes
}
Next we give examples of two interrupt Handlers:
Software implementation of multiply instruction
System call (e.g., printf, open, ...)
Notes: Reg 26 and 27 are temporary registers available to the kernel (specified by Application Binary Interface (ABI))

## Slide 12: SW emulation of MULT instruction
With proper exception handlers we can implement unsupported instructions in SW
MUL returns the low 32-bit result of rs1*rs2 into rd
MUL is decoded as an unsupported instruction and will throw an Illegal Instruction exception
SW handles the exception in illegal_inst_ih() function
  illegal_inst_ih() checks the opcode and function code of MUL to call the emulated multiply function
Control is resumed to epc + 4 after emulation is done (MRET)
mul rd, rs1, rs2

## Slide 13: Illegal Instruction IH (in C)
long illegal_inst_ih(long cause, long epc, long *regs)
{ uint32_t inst = *((uint32_t*)epc); // fetch inst
// check opcode & function codes
if((inst & MASK_MUL) == MATCH_MUL) {
// is MUL, extract rd, rs1, rs2 from inst
int rd = (inst >> 7) & 0x01F;
int rs1 = ...; int rs2 = ...;
// emulate regs[rd] = regs[rs1] * regs[rs2]
emulate_multiply(rd, rs1, rs2, regs);
return epc + 4; // done, resume at epc+4
} else abort();
}

## Slide 14: System call as an instruction
The ecall instruction raises an exception; its meaning is derived based on conventions of the operating system
  Register a7 contains the desired function,
  register a0,a1,a2 contain the arguments,
  result is returned in register a0
Single-cycle implementation: next few slides
Processor can’t function without the cooperation of the software
a0 – a7 are register name aliases (i.e. x10 – x17)

## Slide 15: Syscall Interrupt Handler (in C)
long syscall_ih(long cause, long epc, long *regs) {
// figure out the type of SCALL (stored in a7/x17)
// args are in a0/x10, a1/x11, a2/x12
long type = regs[17]; long arg0 = regs[10];
long arg1 = regs[11]; long arg2 = regs[12];
if(type == SysPrintChar) { ... }
else if(type == SysPrintInt) { ... }
else if(type == SysExit) { ... }
else ...
// ECALL finshes, we need to resume to epc + 4
return epc + 4;
}
Notes: Reg 26 and 27 are temporary registers available to the kernel (specified by Application Binary Interface (ABI))

## Slide 16: Decode
function DecodedInst decode(Data inst, Status status);
DecodedInst dInst = ?; ...
opSystem: begin
case (funct3) ...
fnPRIV: begin // privilege inst
dInst.iType = (case(inst[31:20])
fn12ECALL: Syscall; // sys call
// MRET can only be executed under privilege mode
fn12MRET: isPrivMode(status) ? MRet : NoPermit;
...
default: Unsupported;
endcase);
dInst.dst = Invalid; dInst.src1 = Invalid;
dInst.src2 = Invalid; dInst.imm = Invalid;
dInst.aluFunc = ?; dInst.brFunc = NT;
end ... endcase end
...
return dInst;
endfunction
typedef enum {Alu,...,
NoPermit,Syscall,MRet} IType
Notes: 16
In my version,
Mult (or any unimplemented instruction) gets decoded to
fcMULT, fcMULTU:
begin
dInst.iType = Unsupported;
dInst.dst = Invalid;
dInst.src1 = Invalid;
dInst.src2 = Invalid;
dInst.imm = Invalid;
dInst.brFunc = NT;
end

## Slide 17: Add Execute code for setting CSRs
...
if (eInst.iType==Syscall)
begin
csrf.setStatus(statusPush(csrf.getStatus));
csrf.setCause(32’h08); // cause for System call
csrf.setEpc(pc);
end else
if (eInst.iType==MRet) begin
csrf.setStatus(statusPop(csrf.getStatus));
end

## Slide 18: Redirecting PC single cycle implementation
if (eInst.iType==Syscall)
pc <= csrf.getTvec;
else if (eInst.iType==MRet)
pc <= csrf.getEpc;
else
pc <= eInst.brTaken ? eInst.addr : pc + 4;
Interrupt redirection is done from the last stage; speed is not a paramount concern in hardware handling of interrupts

## Slide 19: Exception Handling in pipelined machines
PC
Inst. Mem
D
Decode
E
M
Data Mem
W
+
Illegal Opcode
Overflow
Data address Exceptions
PC address Exception
External
Interrupts
Ex
D
PC
D
Ex
E
PC
E
Ex
M
PC
M
Cause
EPC
Kill D Stage
Kill F Stage
Kill E Stage
Select Handler PC
Kill Writeback
Commit Point
1. An instruction may cause multiple exceptions; which one should we process?
2. When multiple instructions are causing exceptions; which one should we process first?
from the earliest stage
from the oldest instruction